## Slide 1: Particle Filtering
Edward Wang, Ph.D.

## Slide 2: From Particles to Distribution
Objective: to estimate crack length, ? mm
Expert #1：
2.5 mm
Expert #2：
3.2 mm
Expert #N：
1.8 mm
Initial particle generation
Particle: expert
Particle’s value: crack estimation by expert
Data-driven vibration-crack relationship
Vibration RMS: 0.2 V
Crack length: 2.8 mm
Expert #1：
80% Trust
Expert #2：
75% Trust
Expert #N：
20% Trust
…
…
Particle weight generation
weight: expert’s trustworthiness
By comparing to sensor data
Vibration sensor measurement
crack
3
2
Trust
Distribution generation
Distribution: statistical sum of experts’ estimations
May or may not be Gaussian
The probability distribution provides a measure of uncertainties from experts’ experience and sensor measurement
Notes: This is the first slide to introduce/define what PF is. The slide indicates that particle can be regarded as a human expert. But by definition, what IS a particle, exactly? Do we call it an “agent”? Or a virtual something …?
PW: particle is actually a data point.

## Slide 3: From Particles to Distribution: Illustration
Posterior PDF to be estimated
e.g. normal distribution N(5, 2)
Particles initially sampled from a “guessed” distribution, e.g. uniform U(0, 10)
Weight update
  Statistical sum of particles’ locations forms the estimated distribution
  Estimation accuracy (resolution) increase with increase of particle number
  The accuracy of “guessed” distribution affects PF performance
  Each particle is characterized by two attributes: value (xi) and weight (wi)
  Particles’ weights contribute to estimation of probability at certain values
  Weights initially assigned to be equal
given a new measurement value z=5
Notes: N(5,2): mean value is 5, Std. dev. Is 2
Initial weight assignment: weight of individual particle X number of particles = 1
The process shown in the slide graphly describes sequential importance sampling (SIS)

## Slide 4: Effect of Particle Number on Accuracy
200 particles
500 particles
Histogram
Random Samples
Distribution
1,000 particles
5,000 particles
10,000 particles
Weight
Estimated Distribution
  Example: particles sampled from a Gamma distribution Gamma (4, 1)
  Statistical sum of particles’ locations forms the estimated distribution
  More particles sampled
  → estimated distribution curve is more smooth
  → estimated distribution is closer to the theoretical one

## Slide 5: Particle Filter
System performance degradation
Each particle describes a specific state value and two parameters
System state (e.g. tool wear) at a certain time is the statistical sum of values from a chosen number N of particles, expressed as a probability distribution
Particles’ weights recursively updated given historical measurement
State propagation is predicted as progressive calculations upon prior PDF and lastly updated weights
Computed from prior knowledge
Recursively updated
Measurements
Failure threshold
Current time
Predicted PDF of remaining life
Time, t (Min)

## Slide 6: Particle Filter: Importance Sampling
  Sampling particles from a posterior PDF to be estimated: not possible!
  Alternative approach: sampling from a importance density function (IDF) q
  Weights of particles (importance of particles) updated as
  Good choice of IDF: prior PDF, hence weight update is only related to likelihood function, easy to implement
New meas.
probability
state
weight
Particle value
IDF: even distribution
weight
Particle value

## Slide 7: Sampling Degeneration
  Likelihood calculated from the distance between new meas. and predicted meas. g(x)
  The larger likelihood, the larger updated weight
  Particle degeneracy problem: caused by the mismatch between guessed prior PDF and posterior PDF
  weights concentrate on a few particles, with rest particles contribute nothing to estimation but still consume computing resource
  Candidate solution: resampling, removing particles with small weight

## Slide 8: Sample Degeneration: Illustration
Posterior PDF to be estimated
Sampled particles
Weight update @ 1st iteration
Weight update @ 1st iteration
Sampled particles
  PF performance varies with the accuracy of the “Guessed” distribution from which particles are sampled
Notes: Prior pdf to be estimated N(5,2)
20 particles sampled from [0 10] even distribution; particles are described by two attributes: particles’ values and particles’ weights
With new measurement, particles’ weights are updated. The statistical sum of particles is the estimation of the posterior PDF.
The prerequisite for good estimation is that distribution form which particles are sampled from and the distribution to be estimated should be within the same range. However, in reality, we cannot make a perfect guess. I will introduce in the following.
Another question should be pay attention is the particles’ number. The more particles, the better estimation resolution.

## Slide 9: Particle Filter: Resampling
Arulampalam, A tutorial on particle filter, IEEE Trans. Signal Processing, 2002
New meas.
  Resampling introduced to improve numbers of active particles and computing efficiency
  Sequential Importance Resampling (SIR): comparing particles’ weights to a random number within 0~1to determine particles’ importance
  Particle impoverishment problem: single particle may be selected for multiple times
  The fact that positions of particles remain same since initial sampling is not addressed
state
weight
Particle value
IDF: even distribution
weight
Particle value
weight
Particle value
  Sample degeneracy : caused by the mismatch between prior and posterior PDF
Notes: Resampling: eliminate particles with small weights and keep particles with large weights, implemented by comparing particles’ weights to random numbers.

## Slide 10: Flowchart of Generic PF
Initialize PF Parameters
Propose Initial Population , <x0,w0>
Propagate Particles using State Model , xk-1xk
Update Weights, wk-1wk
Measurement
zk
Weights degenerated?
Resample
Yes
No
  Measure of degeneracy: effective sample size
  Resample whenever

## Slide 11: Particle Impoverishment vs. Time-Varying System
Posterior PDF to be estimated:
A shifting normal distribution, with mean value shifted from 5 to 9.5 in 10 iterations
Particles initially sampled form a “guessed” distribution:
Uniform distribution U(0, 10)
Weight update by standard PF
Given measurement 5 @ 1st iteration, 5.5 @ 2nd iteration,…, 9.5 @ 10th iteration
  Root cause for particle impoverishment
  Particles’ positions remain the same in the resampling
  Particles cannot follow the variation of the posterior PDF
Notes: Prior pdf to be estimated N(5,2)
20 particles sampled from [0 10] even distribution; particles are described by two attributes: particles’ values and particles’ weights
With new measurement, particles’ weights are updated. The statistical sum of particles is the estimation of the posterior PDF.
The prerequisite for good estimation is that distribution form which particles are sampled from and the distribution to be estimated should be within the same range. However, in reality, we cannot make a perfect guess. I will introduce in the following.
Another question should be pay attention is the particles’ number. The more particles, the better estimation resolution.

## Slide 12: Improvement on Particle Filter: Variants
Markov Chain Monte Carlo (MCMC)
Sampling particles by constructing a Markov Chain through a kernel-based transition
Resampling according to Gibbs or Metropolis rule
Regularized PF (RPF)
Create a continuous approximation of posterior PDF for resampling
Continuous PDF is converted from discrete PDF using a Epanechnikov kernel
Auxiliary PF (APF)
Switch the order of sampling and resampling
An auxiliary variable introduced to label particles with high likelihood
Extended Kalman PF (EKPF)
Particles sampled from a normal distribution that is generated by EKF
Introduction of EKF move particles toward high likelihood area
Improving
Sampling
Improving Resampling
Unscented PF (UPF)
Particles sampled from UKF generated normal distribution
Stronger capability in handling nonlinearity than EKPF
Gaussian-Hermite PF (GHPF)
Particles sampled from a normal distribution through Gaussian Hermite integration
Better accuracy than EKPF

## Slide 13: MCMC PF
Time
Weight
k-1
1/N
k-1
1/N
Prediction
1/N
Standard Resampling
  Improvement built upon standard resampling
  Particles resampled from a Markov chain (by adding noises to existing samples); newly particles are accepted if they have better likelihood than the old particles
wk-1
Weight Update
Observation
k-1
1/N
Resampling
Determining Acceptance
Higher likelihood
Yes, keep the newly resampled particle
No, remain the old sample
k
1/N
End of Resampling

## Slide 14: Regularized PF
Time
Weight
k-1
k-1
1/N
1/N
wk-1
Prediction
Weight Update
1/N
Standard Resampling
k
1/N
Resampling
  Improvement built upon standard resampling
  Particles resampled from a continuous distribution (constructed through kernels) instead of discrete positions
Observation
k-1
1/N
Kernel Construction
Kernel
Musso, Improving regularized PF, Sequential MC Methods in Practice, 2001

## Slide 15: Regularized PF: Kernels
  Find a mapping Φ such that, in the new feature space, problem solving is easier (e.g. nonlinear to linear)
  Easy generalization of dot-product (or distance, represents the similarity between objects) based pattern recognition algorithms
Intuitive idea
Commonly used kernels in Regularized PF
  Gaussian kernel
  Epanechnikov kernel

## Slide 16: Numerical Study and Performance Comparison
For PF and its variants, 20 particles are used

## Slide 17: Numerical Study and Performance Comparison
 | EKF | UKF | PF | RPF | MCMC-PF
RMS | 6.11 | 4.87 | 5.98 | 2.11 | 2.51