## Slide 1: Bayesian Inference and Kalman Filtering
Edward Wang, Ph.D.

## Slide 2: Prognostic Elements
Vibration sensor #1
Vibration signal #1
Vibration signal #2
Vibration sensor #2
Sensor Measurement
(z1:k)
Current Part Status
(xk)
Future Part Status
(xk+1, k+2, … )
Inference: estimate system/part current state, based on current measurement
Tracking: identify propagation of state using historical measurements (recursive inference)
Prognosis: predict state propagation in the future, without available measurement
Investigated part
Part State Propagation
(x1:k)
Inference
Tracking
Prognosis
zk

## Slide 3: Prognostic Modeling: Pattern Discovery
Axis Drive
Current/power
Velocity
Position
Ball Screw
Force
Spindle Motor
Current/power
Speed
Position
Force/Torque
Machine Structure
Vibration
AE
Cutting Process
Cutting force
AE
Vibration
Online Measurement
Offline Measurement
Microscope
  From sensing data to system performance
  From sensing data variation pattern to system performance degradation pattern

## Slide 4: Physical Modeling: Force vs. Wear
Instantaneous angle of rotation
Axial depth of cut
Feed rate
Force and chip constant
Chip thickness
  Tangential cutting force vs. process parameters [1]
  Proportional to process parameters, i.e. depth of cut and feed rate
  Independent of cutting speed, neglecting the effect of strain rate on cutting force
  Related to chip thickness
  Tangential cutting force vs. flank wear [2]
  Proportional to sliding friction and width of flank wear VB
Coefficient of sliding friction
Material hardness (e.g. Brinell number)
[1] Altintas and Yellowley, In-process detection of tool failure, J. Engr. Industry, 1989
[2] Shao et al., A cutting power model for tool wear monitoring, J. Machine Tools and Manufacture, 2004

## Slide 5: Physical Modeling: Crack Propagation
Variable | Physical Meaning | Value
R | Stress ratio | 0.7
f | Threshold stress intensity factor | Approximated by crack function [2]
∆Kth | Critical stress intensity factor | A function of f [2]
Kmax | Maximum stress intensity factor | ∆K(1-R)
KC | Fracture toughness | 27.7
C; m; p; q | Constant | 6.23e-9; 2.18; 0.5; 2
[1] Paris and Erdogen, Critical analysis of crack propagation laws, J. Basic Engineering, 1963
[2] Mettu et al., NASGRO, Technical Report, 1999
[3] Maierhofer et al., Modified NASGRO equation, Inter. J. Fatigue, 2014
  Paris’ Law [1]
  Modeling of entire crack propagation [2,3]
  Describe crack propagation da/dN as a function of stress intensity ∆K and material-dependent parameters, C & m

## Slide 6: Challenges in Prognostic Modeling
Machine performance degradation, subjected to:
Gradual deterioration with time-varying degradation rates or modes
Abrupt fault, leading to transient performance changes
Process-to-process variation, non-Gaussian distributions of machines’ status under same operating condition
(Ortiz and Kiremidjian, Engineering Fracture Mechanics, 1988)
(FEMTO-ST bearing dataset, 2012)
Machine tool performance degradation
Bearing performance degradation
Failure threshold

## Slide 7
Uncertainties with Prognostic Modeling
Uncertainty
Process
Varying operating & environmental condition
Joint nonlinear effect of process parameters
Process-to-process variation
Measurement
Measurement noise & sensor failure
Nonlinear relationship between system state and measurement
Modeling
Linear vs. nonlinear
Simplification and assumptions
Gaussian vs. non-Gaussian
(Astakhov, J. Adv. Manuf. Tech., 2007)
(Ortiz, Engr. Fracture Mechanics, 1988)
(Chinchanikar, Materials Science, 2014)
(Saxena, IJPHM, 2016)
Notes: Time-varying degradation: due to varying operational, usage, and load
Measurement error: sensors usually manifest them not as accurate and precise as they are designed, and sensor failure
Nonlinear relationship: tool wear and vibration are not the same physical quantities
Modeling error: due to improper assumption and simplification maded in modeling process

## Slide 8: Stochastic and Probabilistic Modeling
Sensor Measurement
(z1:k)
Inference
Estimate the current system state through a posterior PDF (1), realized via Bayes’ Rule (2)
Current Part Status
(xk)
Tracking
Identify the state propagation model (or recursively update the prior PDF) through a series of posterior PDF, following a Markov process (3)
Prognosis
Predict the future state using the identified state propagation model (a series of prior PDF)
Force signal #1
Force signal #2
zk
Part State Propagation
(x1:k)
Future Part Status
(xk+1, k+2, … )
(1) PDF: Probability Density Function
(2) Bayes’ Rule: posterior PDF can be estimated through prior pdf and likelihood
(3) Markov process: current state xk only dependent on preceding state xk-1
Posterior PDF
Prior PDF
Likelihood
Constant

## Slide 9: Realization: Bayesian Inference
1. Assuming starting with state xk-1 at time k-1
2. Subsequent state xk at time k can be initially predicted using prior PDF, with variance ↑
state
probability
state
probability
state
probability
zk
Following a Markov process
Variance increases as prediction is directly based on assumed prior PDF, without guidance from updated observation
3. With updated measurement (observation) zk
Predicted state will be corrected

## Slide 10: Realization: Bayesian Inference
state
probability
state
probability
state
probability
state
probability
4. Predicted state xk can then be corrected using Bayes’ rule, leading to a decreased variance ↓
  Posterior PDF is calculated by the product of likelihood function P(zk | xk) and prior PDF
  Extent of correction is determined by the confidence (or uncertainty level) of prior PDF and measurement
  Correction is implemented by Kalman filtering (KF) or particle filtering (PF)
zk
1. Assuming starting with state xk-1 at time k-1
2. Subsequent state xk at time k can be initially predicted using prior PDF, with variance ↑
3. With updated measurement (observation) zk

## Slide 11: Bayesian for State and Parameter Estimation
x
y
(xk-1, yk-1)
(xk, yk)
  State estimation P(x|z)
  State evolution model is known
  e.g. object tracking (car running on a linear road with constant speed)
  Joint state and parameter estimation P(x,θ|z)
  State evolution is dominated by unknown parameters
  e.g. car running with unknown speed
Speed , (parameters) need to be estimated first, then position (state)

## Slide 12: Determine Prior PDF and Likelihood Function
Prior PDF
Parameters to be estimated
System state at time k
Process-to-process variation
  Also called State Evolution model
  Usually obtained from physical or empirical knowledge
  Sometimes conditional on parameters, {Ak, Bk}, related to system operating conditions
Likelihood Function P(zk | xk)
Measurement noise
Sensor data or extracted features
  Also called Measurement model
Paris law, describing crack propagation over time (i.e. from xk-1 to xk)
System state at time k
a: crack length
N: cut number
K: range of stress intensity

## Slide 13: Gaussian vs. Non-Gaussian Inference
  Gaussian distribution
  Can be fully characterized by first two moments (i.e. mean and variance)
  Straightforward to find optimal estimation of unimodal distribution
exponential distribution
Multimodal distribution
Exponential
Not exact Gaussian
  Non-Gaussian distribution
  Conditional PDF of state on time-varying parameters may follow an exponential or multimodal distribution
  Can be approximated by random sampling methods, e.g. particle filter
State evolution model:
Measurement model:
  Variation or Noise (wk, vk) can be Gaussian or Non-Gaussian

## Slide 14: Linear vs. Non-Linear Inference
State evolution model:
Measurement model:
g1
g2
  Case 1: f or g is non-linear but continuous
  Extended Kalman Filter (EKF) through linearization
  Unscented KF through nonlinear transformation
  Particle Filter (PF) through random sampling
  Case 2: f or g is non-linear but piecewise
  Switching or interacting KF/PF (multiple mode KF/PF)

## Slide 15: Bayesian Probabilistic Modeling Methods
  Methods for calculating posterior PDF
Sikorska et al., Prognostic Modelling Options for Remaining Useful Life Estimation. Mechanical Systems and Signal Processing (2013)

## Slide 16: Kalman Filter (KF)
  Describe a PDF with mean and covariance, thus has the Gaussian assumption
  Obtain the optimal estimation by minimizing mean squared error of the estimation
state
probability
state
probability
state
probability
state
probability
zk
Assume
State model
Meas. model
Covariance of process and meas. noise
Prediction
State
Covariance
Update
State
Covariance
Recursively decreasing
Kalman gain
Equal mean, larger covariance
Covariance ↓

## Slide 17: Extended Kalman Filter (EKF)
  If the state and measurement models are non-linear, standard KF does not work
  EKF: use Taylor Series to linearize the models
State model
Meas. model
Prediction
State
Covariance
Update
State
Covariance
KF and EKF can only be applied to Gaussian System that states, parameters and measurements are assumed to follow Gaussian distributions, which may or may not be valid in practice

## Slide 18: Simulation