## Slide 1: Overview of Process Monitoring
Edward Wang, Ph.D.

## Slide 2: Manufacturing Processes
Milling
Turning
Injection Molding
Stamping
Additive Manufacturing
Notes: Milling vs turning: 1. flat vs. cylindrical surface, 2. single point vs. multi-point cutter, 3. cutting speed provided by rotating cutter vs. workpiece

## Slide 3: Process Monitoring
Speed
Cutting depth
Feed rate
Product Level (product quality)
  Dimensional accuracy, surface roughness, residual stress
Process Level
  Manufacturing efficiency (cycle time), energy efficiency, material efficiency
Machine Level
  Condition (chattering), tool wear, crack, failures of mechanical parts
Notes: Residual stress, caused by mechanical and thermal loads, as well as phase changes, leads to fatigue, component distortion and crack

## Slide 4: Process Monitoring
Machine
Process
Material
Control inputs
Energy
Product-Level Attributes
Process-Level Attributes
Machine-Level Attributes
?
Sensing
Data Analytics
Notes: Can control inputs/machine settings determine solely the attributes?
NO.
Because of process-to-process variation, environmental disturbance, variations in materials and other disturbance
The goal is to accurately estimate the attributes based on both control inputs and in-process sensing

## Slide 5: Sensing: Historical Perspective
Dynamo, designed by Hippolyte Pixii
1830
Electric Generator
Modern Lathe
1910
Ancient Manufac.
Crossbow Trigger
Qin Dynasty
230 B.C.
CNC Machine
1960
Additive Manufac.
Metal powder freeform fabrication
Electric ally powered, reproducibility
2010
Egyptian Ruler
3000 B.C.
Seebeck & Thermocouple
1821
1919
Barometer
1843
MEMS Sensor
1990
1950
Piezo Sensor
Photodiode
Laser Cutting
1970
Programmable, multiple functions
New tooling, energy
Fluid-Gas Pressure
Mechanical-Electrical
Photo-Electrical
Microelectro-mechanical
Thermal-Electrical
Calibration & Standard
Notes: Piezoelectric Effect is the ability of certain materials to generate an electric charge in response to applied mechanical stress
Photodiodes may contain optical filters, built-in lenses, and may have large or small surface areas

## Slide 6: Sensing Principal: Signal Transduction Mechanisms
 | Mechanical | Thermal | Electrical | Magnetic | Radiant
Mechanical | Mechanical and Acoustic Effect | Friction, Cooling | Piezoelectric, Piezoresistive Effect | Magneto-mechanical | Photoelastic, Sagnac, Doppler
Thermal | Thermal Expansion, Radiometer Effect |  | Thermo-resistive/capacitive, Seebeck, Pyroelectric Effect |  | Radiant Emission, Thermo-optical Effect,
Electrical | Electromechanical, Electrokinetic Effect | Joule Heating, Peltier Effect | Charge Collectors, Langmuir Probe | Biot-Savart’s Law | Electro-optical Effect
Magnetic | Magnetomechanical Effect | Thermo-magnetic Effect | Galvanomagnetic Effect |  | Magnetooptical Effect
Radiant | Radiation Pressure | Bolometer, Thermopile | Photoelectric Effect |  | Optical Bistability, Photorefractive Effect
Chemical | Electrodeposition, Photoacoustic Effect | Calorimeter, Thermo-conductivity | Potentiometry, Gas Sensitive Field, Conductimetry, | Nuclear Magnetic Resonance | Spectroscopy, Chemiluminescence
Electromagnetic Inference Detection
Displacement/Proximity Sensing
Temperature Sensing
Displacement/Deformation Based Force Sensing
Measurable Parameters
Acoustic Discharge Mapping
Residual Stress Measurement
Physical Effects
Process Characterization
Notes: The piezoresistive effect is a change In the electrical resistivity of a semiconductor or metal when mechanical strain is applied
The thermoelectric effect is the direct conversion of temperature differences to electric voltage and vice versa via a thermocouple
Pyroelectricity is a property of certain crystals which are naturally electrically polarized and as a result contain large electric fields. Pyroelectricity can be described as the ability of certain materials to generate a temporary voltage when they are heated or cooled.
A galvanomagnetic effect is described which is observed by measuring the induced voltage normal to the direction of current flow as in the Hall effect but with the magnetic field in the current-voltage plane. Can be used for electrical discharge machine monitoring (so called wire burning)
The photoelectric effect is the emission of electrons or other free carriers when light hits a material. Electrons emitted in this manner can be called photoelectrons. This phenomenon is commonly studied in electronic physics and in fields of chemistry such as quantum chemistry and electrochemistry

## Slide 7: Sensing for Manufacturing
Product Dimension | Dimension Material flow | Product dimension
Chatter marks Tool wear Crack generation | Flatness Strip rupture | Surface quality
Residual Stress Tool Wear | Forming depth | 
Surface hardness Residual stress |  | Porosity Residual stress
Manufacturing
Subtractive Manufact.
Additive Manufacturing
Cutting
EDM
Net Shaping
Stamping
Rolling
−
+
Position/Dist.
Vibration
Force/Pressure
Temperature
Grinding

## Slide 8: Tool Wear Monitoring & Prognosis

## Slide 9: Tool Wear and Life Prognosis
Force
Vibration
Acoustic Emission
Monitoring
……
Tracking and prognosis
Model physical mechanism of tool wear propagation
Predict wear propagation under given operation conditions and materials
Quantify uncertainty due to process-to-process variations and measurement error
Prognosis of Wear:
AE amplitude distribution within one cut
Probability

## Slide 10: Tool Wear Initiation and Propagation
Chart: Feed rate (mm/rev)
| 0.1 | 0.13 | 0.16 | 0.19 | 0.22 | 0.25 | 0.28000000000000003 | 0.32 | 0.38 | 0.43
v =120m/min | 7.8 | 6.1 | 4.2 | 3.2 | 2.8 | 3.2 | 4.1 | 5.2 | 6.4 | 7
v = 90m/min | 5.2 | 3.1 | 2 | 1.7 | 2.1 | 2.7 | 3.6
v = 60m/min | 4.3 | 2.8 | 2.2 | 1.6 | 1.2 | 1
Abrasion area
Tool
Clearance face
Rake face
Flank wear
Work piece
Friction
Crater wear
Cutting direction
Chip
  Common tool wear types
  Flank wear: caused by friction between tool clearance surface and workpiece
  Crater wear: caused by friction between rake face and chip
  Tool wear leads to poor surface finish and increase in power consumption
  Effect of machine settings on tool wear
  Increased cutting speed: increase in cutting temperature, shortened tool life
  Increased feed rate & depth of cut: quadratic relationship between tool wear and feed rate
Astakhov, J. Adv. Manuf. Tech., 2007

## Slide 11: Tool Wear Propagation Modeling
Tool life model | Tool wear rate model
Taylor’s tool life equation: VLn=C1 (L: life, V: cutting speed, n,C1=const.) | Paris law: dx/dt = CΔKm (x: wear width; C, m = const.)
Taylor’s extended equation: L = C2/(Vpfqdr) (f: feed rate, d: depth, p,q,r,C2=const.) | Takeyama & Murata’s wear model: dx/dt = G(V,f)+Dexp(-E/RT) (E: energy, R,G,D = const.)
Hastings tool life equation TLn=C3 (T: temperature, n, C3=const.) | Usui’s wear model dx/dt = AσnVsexp(-B/T) (σn: stress, A,B = const.)
Wear propagation model (derived from Paris law)
Relate wear to stress intensity factor
Wear width
Number of load cycles
Material-related parameters
Stress intensity factor
Stress range: constant
Schrock, Phase dependent tool wear, J. Manuf. Sci. Eng., 2014

## Slide 12: Process Monitoring in Injection Molding

## Slide 13: Injection Molding of Polymers
Role in manufacturing
  Invented in 1872 by John Wesley Hyatt
  Processing 32% of all plastics products;
  Producing 10,000 – 1,000,000 parts per mold
Hopper
Raw Polymer
Injection Drive Motor
Screw
Mold
Clamp Drive Motor
Nozzle
Barrel
Heater Bands
Screw Drive Motor
Hydraulic Pump
Cavity, in which parts are produced
  Pressure Level: 50~100MPa
  Ramping Rate:
  < 100MPa/sec
  Temperature：
      Melt: < 400oC
      Mold: 80~200oC

## Slide 14: Information Feedback
Three levels of information feedback:
  Machine: far away from mold cavity, only global information
  Process: a level closer, but still no accurate correlation with part quality
  State: directly relates part quality to melt and mold for optimal control – desired!
Need: sensor measuring multiple parameters, remote data retrieval through RF-shielded mold steel

## Slide 15: Molding Process Monitoring

## Slide 16: Sensing Modality vs. Part Quality
52.5% of part quality can be explained by retrieving and analyzing information on melt pressure;
Improvement of up to 92.5% can be expected if melt temperature, velocity, and viscosity can be include in the measurement.

## Slide 17: Sensing Principle
Sensing Parameters
Melt pressure
Melt temperature
Melt velocity
Melt viscosity
Piezo-Ceramic Ring Stack
Infrared Detector (thermopile)
Physical Sensors
Inferencing
Pressure Ramping Rate
Temperature Ramping Rate
Viscosity and Velocity determined through inference from P and T measurements

## Slide 18: Multivariate Sensing
Acoustic Wireless data transmission
  Immune to electro-magnetic shielding
  No through hole to be drilled on mold for remote data retrieval
Multivariate Sensing (MVS)
4 parameters/sensor package
  Pressure
  Temperature
  Velocity
  Viscosity

## Slide 19: Mechanisms for Data Transmission
Data Transmission
Wireless advantages
  Improved flexibility for sensor deployment
  Minimized modification on machine structure
  Reduced cost on installation and maintenance
Wired
Transmission
Electromagnetic
Waves
Acoustic
Waves
Requires drilled holes, Intrusive
Not feasible for RF-shielded media
Non-intrusive, propagates in RF-shielded media
Acoustic modulation
Wave propagation
Feature extraction
Acoustic Transmission

## Slide 20: Acoustic Wave Propagation
20 Hz
20 kHz
2 MHz
200 MHz
100 kHz
Properties:
  Longitudinal wave, particle movement direction in parallel with propagation direction
  Propagate via compression and decompression of medium materials
Interfere with structural vibration in manufacturing machines
High attenuation,
wavelength → metal crystal dimension (mm level)
500 kHz ~ 2 MHz
Chosen for acoustic data transmission

## Slide 21: Acoustic Signal Transmission
{81, 82, 83, 85, 90…}
Unit: [ oC ]
{24, 33, 45, 59, 61…}
Unit: [ MPa ]
{200, 211, 232, 217…}
Unit: [ mm/s ]
Data (Decimal)
{01010001 (81)….}
Digits (Binary)
{00011000 (24)….}
{11001000 (200)….}
Goal: To transmit multiple parameters through metal using acoustic wave as info carrier
Challenges
  Determine carrier frequencies for modulation.
  Design transmitter to convert modulated signal into acoustic wave.

## Slide 22: Process Monitoring in Stamping

## Slide 23: Stamping
Salient Features
  Fast operation
  Cold working improves stiffness
Widely Used
  Cans (230x109 cans/year)
  Automobiles (300+ parts/car)
  Aviation, naval, etc.
Motor Vehicle Metal Stamping Industry in the U.S. and its Foreign Trade
Study Report, Supplier Relations, March 2009
$20.6 B revenue in 2008 for automobile industry

## Slide 24: Stamping Process
Mechanism
  Stamping of sheet metal
  Tools: binder, punch, and die
Steps
  Edges of sheet clamped by binder
  Sheet formed into die cavity by punch

## Slide 25: Workpiece-Tool Interaction
Variations in the tool-workpiece interaction lead to defective parts
Causes:
  Die misalignment
  Uneven binder pressure
  Slide non-parallelism
  Shut height variation
  Die flexing
  Lubricant distribution
  Spring back
Spatio-temporal Contact Pressure Distribution aids in defect detection
Other benefits
  Understanding process mechanism
  Tool wear monitoring
  Better tool designs
Section of
Stamping Setup
Some Common Defects

## Slide 26: In-Die Pressure Sensing
Ink based systems
  Plastic films with ink microcapsules
  Pressure burst capsules, color intensity indicates pressure
  Static measurement – single use
  May wrinkle or tear on 3D shapes
Matrix systems
  Matrix of small piezo-resistive or piezo-electric elements
  Dynamic measurement
  Can not be used on 3D shapes
  Limited range (e.g. 863 kPa)
50 mm
2 mm x 2 mm
25 x 25 array
30 cm
32 x 32 array
Discrete sensors
  Thin film button cells
  Quartz dynamic force sensors
  Divide force by sensing area
TF Sensor
Dynamic Force Sensors

## Slide 27: Sensor Integration Techniques
Two methods investigated
  Bottom mount: Sensor installed in a blind hole drilled from the back of die. Die working surface not altered in any manner. Sensor behavior is controlled by the embedding depth
  Top mount: Sensor installed in a hole drilled in the working surface of the die. Sensor behavior controlled by the clearance
Bottom Mount
Top Mount

## Slide 28: Pressure Sensing
Top mount: local pressure distribution studied by matrix sensor with 625 elements
High clearances (~0.001” or 25.4 μm) disturb original pressure distribution
Assembly Process
Ground Finish
0.0005” or 12.7 μm
0.001” or 25.4 μm
0.002” or 50.8 μm
Flat Surface
Cylindrical Surface
Minimum Disturbance
Distortion of original pressure distributions
Cylindrical
Contact Surface
Flat
Contact Surface
Matrix Sensor
25 x 25
50 mm
Sensing Element
2 mm x 2 mm
50 mm
Sampling: 100Hz
Range: 125 PSI/ 863 KPa
KPa
Net Testing Force : 200 N (Limited by matrix sensor range)
Piezo Quartz Sensor
R = 10 mm
Range: 10 KPSI/ 70 MPa

## Slide 29: Pressure Reconstruction
Tool-workpiece interaction governed by contact pressure
Pressure sampled by sensors at discrete locations
Seek mathematical techniques for pressure reconstruction
Estimated
Pressure
. . . . . . . . . .

## Slide 30: Process Monitoring in Chemical Mechanical Polishing Process

## Slide 31: CMP
(Borst et al., Thin Solid Films, 2001)
  A process of planarizing wafer surfaces by using a combination of chemical reactions and mechanical forces
  The global CMP market: $3.32 Billion in 2014, and is estimated to reach $ 4.94 Billion by 2020 (with rate of 6.83%)
63.1 nm
10.7 nm
5.8 nm
Before CMP
After 1st CMP
After 2nd CMP
(Sung et al., Ultra-smooth BaTiO3 surface morphology, Materials Science in Semiconductor Processing, 2015)
RMS of surface protrusions
Notes: Copper Electrochemical Deposition (ECD): a process used for plating copper electrical conductor on printed circuit boards
TaN: the abbreviation for Tantalum, a chemical element. TaN barrier is to prevent copper (Cu) diffusion into the silicon

## Slide 32: CMP Mechanism
  Chemical reaction
    Hydroxyl ions attack SiO2 in oxide CMP, causing surface softening and chemical dissolution
    Oxidants enhance metal dissolution and control passivation in metal CMP
  Mechanical abrasion
    Soften surface removed by abrasives suspended in the slurry and the friction between the pad and the wafer
  Material Removal Rate (MRR): Critical indicator for CMP monitoring
Dow Electronic Materials, Fine-tuning CMP Slurries for 3D TSV Processes, 2017

## Slide 33: Parameters Affecting MRR
Dresser
Conditioning motion
Abrasive type
Abrasive density
Abrasive configuration
Slurry
Type
Abrasive size
pH Value
Abrasive hardness
Concentration
Flow rate
Additive
Zeta potential
Others
Temperature
Polishing time
Wafer
Pressure
Pattern hardness
Film type
Wafer size
Pad
Hardness
Compressibility
Relative speed
Worn degree
MRR [nm/min]

## Slide 34: MRR Modeling
  Model 1: Pressure and relative rotational speed
Constant
Pressure
Relative speed
[1] Preston, J. Society of Glass Technology, 1927
[2] Tseng and Wang, J. Electrochemcial Society, 1999
[3] Figure from Klocke and Zunke, CIRP Annals, 2009
  Model 2: Abrasive number, geometry, pad hardness and deformation
Wafer density
Abrasive number
Removal by single abrasive
(Luo and Dornfeld, IEEE Semiconductor Manufacturing, 2001)
    Preston Equation [1]
    Exponential coefficients, α and β, vary with wafer materials, within [0, 1] [2]
Abrasive size
SSiC: sintered silicon carbide
HIPSN: hot-isostatically pressed silicon nitride
Ceria: ceria oxide
Zirconia: Zirconium oxide
b: ratio of the real contact area between abrasives and wafer over apparent area, determined by applied pressure on wafer and wafer’s Young’s modulus

## Slide 35: MRR Modeling
  Challenges in modeling MRR:
  Difficult to include all process parameters considered in one model
  Hard to quantitative effect of chemical reaction
  MRR vs. Wafer Hardness
  (Dambon and Demmer, CRIP Annals, 2006)
  MRR vs. Chemical Effect
  (Lee and Jeong, CRIP Annals, 2009)
  MRR vs. Polishing Agent
  (Takaya et al, CRIP Annals, 2011)
  MRR vs. Pad Condition
  (Byrne et al, CRIP Annals, 1999)
MRR nm/min

## Slide 36: Process Monitoring in Additive Manufacturing

## Slide 37: AM: Milestones
1990
2000
2010
2020
FAA approved 3D printed part for Boeing 787
(2017)
First 3D printed organ
(synthetic scaffold)
(1999)
First usable 3D printed prosthetic Leg
(2008)
3D printed blades for GE aircraft engine
(2018)
Representative Applications
Fused Deposition Modeling
(1991)
Selective Laser Sintering
(1991)
Stereolithography Apparatus
(1987)
Polyjet
(2005)
Representative AM Technologies
Stratasys; GE; Boeing

## Slide 38: Major AM Technologies
Filament
Part
Extruder
Platform
Support
Plastic filament melt & deposition
Fused Deposition Modeling (FDM)
Powder feeder
Laser system
Recoater
Powder bed
Part
Overflow bin
Solid powder fusion by laser
Selective Laser
Sintering (SLS)
Elevator
Part
Sweeper
Resin
Laser system
Mirror
Liquid resin hardened by UV light
Stereolithography Apparatus (SLA)
AM technologies: market share
Others
 | Cost | Material | Surface | Strength
FDM | Low | Wide | Rough | Low
SLS | High | Limited | Rough | High
SLA | High | Limited | Smooth | Low

## Slide 39: Fused Deposition Modeling
x
y
z
Platform moves in z direction, allowing part built layer by layer
Acrylonitrile Butadiene Styrene (ABS) or
Polylactic Acid (PLA)
Filament heated over transition temperature before deposition
Nozzle moves in x and y directions, allowing different printing paths

## Slide 40: FDM Process
Stratasys Direct Manufacturing, 2017

## Slide 41: FDM Process: Overview
Strengths
High cost-effectiveness
Wide options of materials
Rapid prototyping
Machine cost ($) | 
FDM | ~2k
SLS | ~150k
SLA | ~80k
Sculpteo, 2017
Limitations
Relatively low precision, surface smoothness, tensile strength (due to low bonding force between layers)
Influenced by multiple process factors, difficult to control the part quality, due to insufficient understanding of process-property relationships
Wu et al., Influence of layer thickness, Materials, 2015
15 layers
Printing speed (mm/h) | 
FDM | 50~150
SLS | Up to 48
SLA | Up to 14
Printed by FDM
Printed by SLS
vs.

## Slide 42: FDM Qualitative Modeling
FDM process traditionally analyzed qualitatively
Experimentally obtained part property variation curve through adjusting process parameters
Substantial understanding and modeling of FDM process
Requires quantitative modeling of process parameters/variables - part property relationship
Provides technology basis for address the part property inconsistency through process parameter optimization
Surface roughness vs.
extruder temperature
Surface roughness vs.
printing speed/feed rate
[1] P Rao et al., Quality monitoring in additive manufacturing, J Manuf Sci Eng, 2015
[2] V Kovan et al., Printing parameters effect, J Mech Sci Technol, 2018

## Slide 43: FDM Quantitative Modeling
Requirements for quantitative modeling of process-property relationship in FDM
Characterize thermal interactions among layers;
Describe effects of process parameters and layers’ interactions simultaneously;
Relate to final part property.
Time (s)
Temperature (℃)
Thermal Behavior
Microstructure
Property
Layer #1
Layer #2
Layer #3
Strain (%)
Stress (MPa)
Process Parameter
Performance
Printing speed
Extruder temp.
Layer height
Material
Surface roughness
Tensile strength
Thermal behavior affected by process parameters
Layers’ interactions affect their microstructure
Joint effect of process parameters and layers’ interactions on property